## Slide 1: Modern Netlist Reversing
Dr. Andrew Zonenberg (@azonenberg)
Senior Security Consultant, IOActive
Robert Ou (@rqou_)
Graduate Student, University of California at Berkeley
Towards a Hardware Decompiler

## Slide 2: About Me
PhD Computer Science (RPI)
FPGA dev and IC RE since 2010
Created and taught first full course on semiconductor reverse engineering ever offered by a university
Embedded pentesting at IOActive since 2015

## Slide 3: The Vision

## Slide 4: The Vision
We want IDA Pro for silicon!
The state of the art in HW RE is decades behind SW
  “Disassemblers” are rare
  “Decompilers” are unheard of
  Some cool academic papers / commercial in-house tools
  Almost no publicly available tooling

## Slide 5: How to Do It
One de-synthesizer per architecture doesn’t scale
Use an IR-based flow
Arch 1
Arch 2
Arch N
IR
Feature
Extraction
Behavioral
Verilog
Un-techmap

## Slide 6: Initial Target Architectures
One product term CPLD and one LUT based FPGA
  Xilinx CoolRunner-II
  Silego GreenPAK4
Small devices, easy to test
Known bitstream structures
  We reversed CR-II (fully, since my REcon ‘15 talk)
  GreenPAK is documented by vendor
(partially) supported by open toolchains

## Slide 7: ASICs
We eventually want to be able to RE arbitrary silicon
Some research at IOA is going in this direction
Nothing worth showing off yet 
Lots of fun linear algebra etc
… but FPGAs let us skip that!

## Slide 8: ASIC front end (wishlist only )

## Slide 9: ASIC front end (by hand)

## Slide 10: Silego GreenPAK4 (SLG46620)
Tiny mixed signal FPGA
FPGA fabric: 26 variable-sized LUTs, 12 FFs
Oscillators
Analog hard IP: Comparators (w/ vref), ADC, DAC
Digital hard IP: counters, sh.regs, compare/PWM

## Slide 11: Silego GreenPAK4 front end (beta)

## Slide 12: Xilinx CoolRunner-II (XC2C32A)
Straightforward PLA-based CPLD
2 function blocks, each with:
  16 GPIOs
  16 macrocells w/ XOR, FF
  80x56 AND array
  56x16 OR array
Global clock/reset trees
One extra input

## Slide 13: Xilinx CoolRunner-II front end (alpha)

## Slide 14: Lattice ice40 (ice40lp1k)
On die OTP
16x10 tiles of 8 LUT4s
4Kb block RAMs
PLLs
Supported by open IceStorm toolchain

## Slide 15: Lattice ice40 front end (alpha)
Use icebox_vlog.py to convert to low level Verilog
Read generated Verilog and untechmap
Not primary development focus for now
As we scale to larger devices, will get more testing

## Slide 16: Native netlist
A sea of standard cells
No structure whatsoever
Unused FPGA cells removed

## Slide 17: Native netlist

## Slide 18: Intermediate Representation
Replace LUTs and library cells with generic equivalents
Generic Boolean logic
Preserve analog/mixed signal IP as instances

## Slide 19: Intermediate Representation

## Slide 20: De-synthesis
Find isomorphisms in IR netlist
Replace them with more abstract equivalents
Use existing coarse-grained synthesis algorithms!

## Slide 21: Shift registers
Already in Yosys for coarse-grained synthesis
But works on raw netlists too!
Find chains of DFF w/ same clk/reset*
* DFFCE needs more work

## Slide 22: Adders
Find half/full adders and chain them
Caveat - Addition is commutative! (see pin 7)

## Slide 23: Multi-bit gates
Combine chains of 2-input gates into larger gates
Yosys considers these reductions of a single vector
Wide gates = comparators etc

## Slide 24: Toggle flipflops
DFF + XOR = TFF
Extracting these makes other structures easier to find

## Slide 25: TFF-Based Counters
Chained TFFs = binary counter

## Slide 26: TFF-Based Counters
Current pass always produces POUT
Comparator not yet absorbed into OUT port

## Slide 27: TFF-Based Counters
Non power-of-two needs more work

## Slide 28: Bus detection
Some blocks have inherent ordering on outputs
Infer multi-bit buses from these
Heuristic: if one input to block is a bus, so is the other

## Slide 29: Bus detection

## Slide 30: DeMorgan for reductions
If &() or |() has lots of inverted inputs, push the inverter
This optimization is useful for synthesis too!

## Slide 31: How about some less trivial tests?
Feature extraction works decently on larger designs
We’re still working on visualizations
Current renderer (Yosys “show” -> xdot) scales poorly
  Long run time to place graph elements
  Non-interactive, can’t move nodes or rename them
  Doesn’t show parameters or attributes well
  Very poor handling of high fanout nets

## Slide 32: LED chaser (GP4)

## Slide 33: LED chaser (GP4)

## Slide 34: 10baseT autonegotiation (GP4)

## Slide 35: 8N1 UART TX (ice40)

## Slide 36: Original UART (TX+RX) pre-techmap
Clearly we have a ways to go!

## Slide 37: Graphviz doesn’t handle clocks well

## Slide 38: Like Pulling Bitstreams
Firmware update files (if cleartext)
If encrypted, DPA usually works
  “Improved Side-Channel Analysis Attacks on Xilinx Bitstream Encryption of 5, 6, and 7 Series”, COSADE ‘16
Hardware defeats of lock bits (if on chip)
Conjecture: Reading antifuses by FIB VC + CV?

## Slide 39: Longer Term Roadmap
Add an interactive GUI
Support for extracting hierarchy and processes
  Most likely human-guided w/ automated implementation
  Draw approximate hierarchy and use min-cut?
Support for more FPGA/CPLD devices
Implement ASIC front end
More advanced analytics

## Slide 40: Longer Term Roadmap
Traceability back to physical layout (for invasive)
Physical IP recognition for ASIC
  Find known SRAM, efuse, PLLs, etc
  Ideally: ML classifier for unknown physical IP?
“FLIRT” for IP cores
  NP-complete in general case 
  Can we use randomization, spatial partitioning, etc?
  Won’t find everything, but is it good enough?

## Slide 41: Get The Code
https://github.com/azonenberg/yosys/ My fork of Yosys with additional RE-focused passes ISC license
https://github.com/azonenberg/openfpga Bitstream support / PAR for CoolRunner + GreenPAK LGPL

## Slide 42: Acknowledgements
John McMaster – wet lab for XC2C samples
Clifford Wolf – lots of new Yosys features

## Slide 43: Fun with XC2C32A “suicide bitstream”

## Slide 44: Questions?